## Slide 1: Arduino Drone
Team 0xDEADBEEF
Ryan Berge and Jeremy DeHaan

## Slide 2: Arduino Drone fan
Team 0xDEADBEEF
Ryan Berge and Jeremy DeHaan

## Slide 3: Project Goals
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection
fan

## Slide 4: Original Part List
3-Axis Analog Gyro
4 USAQ 8520 Coreless Brushed Motors
LiPo Battery 350mAh
LiPo Battery Charger
1 XT60 Power Distribution Board
Half-sized Breadboard PCB
2 Qunqi L298N Motor Drive Controllers
2 HC-05 Bluetooth Transmitter/Receiver
Buzzer
Various LED lights
8 Buttons
Ultrasonic Sensor
Photocell Sensor
3D-Printed Chassis
2 Arduino Mega Boards
SPDC Slide Switch
2 USB Cables

## Slide 5: Final Part List
3-Axis Analog Gyro
4 USAQ 8520 Coreless Brushed Motors
12 USAQ 8520 Coreless Brushed Motors
LiPo Battery 350mAh
LiPo Battery 850mAh
LiPo Battery Charger
1 XT60 Power Distribution Board
2 XT60 Power Distribution Boards?
Half-sized Breadboard PCB
2 Qunqi L298N Motor Drive Controllers
2 HC-05 Bluetooth Transmitter/Receiver
Buzzer
Various LED lights
8 Buttons
Ultrasonic Sensor
Photocell Sensor
3D Printed Chassis
Several 3D Printed Chassis
2 Arduino Mega Boards
1 Mega, 1 Micro
SPDC Slide Switch
2 USB Cables

## Slide 6: Final Part List
3-Axis Analog Gyro
4 USAQ 8520 Coreless Brushed Motors
12 USAQ 8520 Coreless Brushed Motors
LiPo Battery 350mAh
LiPo Battery 850mAh
LiPo Battery Charger
1 XT60 Power Distribution Board
2 XT60 Power Distribution Boards?
Half-sized Breadboard PCB
2 Qunqi L298N Motor Drive Controllers
2 HC-05 Bluetooth Transmitter/Receiver
Buzzer
Various LED lights
8 Buttons
Ultrasonic Sensor
Photocell Sensor
3D Printed Chassis
Several 3D Printed Chassis
2 Arduino Mega Boards
1 Mega, 1 Micro
SPDC Slide Switch
2 USB Cables
Balloons

## Slide 7: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 8: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 9: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 10: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 11: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 12: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 13: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection

## Slide 14: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection
Drone Actually Flies

## Slide 15: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection
Drone Actually Flies

## Slide 16: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection
Drone Actually Flies

## Slide 17: Final Product
Original Goals:
Create a Quad-Copter Arduino Remote-Controlled Drone
Wireless Bluetooth Communication for Control Pad
Automatic Take-Off and Landing Procedures
Automatic Stabilization
Music
Low-Light Detection
Drone Actually Flies
fan
fan

## Slide 18: Problem?

## Slide 19: Problem?
Drone is too heavy.

## Slide 20: Problems Along The Way
Bluetooth HC-06 would not enter AT-Command Mode
3D-Printers warped drone parts
3D-Printers overheated and stopped halfway through
3D-Printers were unavailable
Motor Controllers don’t accept enough voltage
Ran out of female-to-female jumper cables
Bellevue store had only two 1.6mm screws
Motor Controllers overheating?

## Slide 21: Problems Along The Way (continued)
Motor Controllers are too heavy
Burned out the battery
Drone was too heavy
Drone was too heavy again
Buzzer does some weird things with PWM signals
Buzzer turns off motors?
Propeller flies off the drone
Mosfets melt the chassis

## Slide 22: Problems Along The Way (continued again)
Ultrasonic Sonar gives inconsistent data
IMU overflows FIFO buffer
Navigation loop too sensitive
Navigation loop not sensitive enough
Bluetooth sometimes doesn’t connect
Motors have inconsistent speeds
Motors pull more current than they’re supposed to
Built-in Analog-to-Digital circuit does weird things

## Slide 23: Still More Problems
Propellers are still flying off
Accidentally destroyed the V-in pin
Accidentally sending power in the wrong direction
Photocell is broken
Diagnostics LED blinds you if you put your face next to it
Drone isn’t stable even when in the air
Micro doesn’t have very many pins
Especially PWM pins

## Slide 24: Interesting Problems
Bluetooth
Buzzer
Power

## Slide 25: Drone Designs

## Slide 26: Drone Designs

## Slide 27: Drone Designs

## Slide 28: Drone Designs

## Slide 29: Drone Designs

## Slide 30: Drone Designs

## Slide 31: Drone Designs

## Slide 32: Drone Designs

## Slide 33: System Components
Photocell
Diagnostic LED
More Motors
IMU
Power Switch
Motors
Bluetooth

## Slide 34: Controller Components
Cardboard
Button
Button
Button
Button
Button
Button
Button
Button
LED

## Slide 35: Controller (inside)
Arduino Mega
Wires
Bluetooth

## Slide 36: Drone Systems
Communication
  2-way Bluetooth between Drone and Controller
  Controller receives input from buttons, sends commands to drone
  Controller receives data from drone, prints to serial monitor
Navigation
  Drone supports multiple states: Landed, Flying, Taking Off, Landing, Testing
  Motors are adjusted to achieve some desired state
  Commands sent over Bluetooth modify desired state
Diagnostics
  Send data back over Bluetooth
  Programmable LED provides system-critical information

## Slide 37: Sensors
Inertial Measurement Unit (IMU)
  Keep track of Pitch and Roll
Ultrasonic Sonar System
  Keep track of altitude (for use in take-off and landing procedures)
Photocell
  Keep track of ambient light levels
Battery Charge
  Detect low-battery (doesn’t really work)

## Slide 38: Estimated System Cost
Chassis ---------------------------------------------------------------------------------------------------------- 3D printed: cost unknown
Motors, x8 ----------------------------------------------------------------------------------------------------- $28
Arduino Micro ------------------------------------------------------------------------------------------------- $25
Mosfet Circuit, x8 --------------------------------------------------------------------------------------------- $14
Mosfet Heat Skinks, x8 -------------------------------------------------------------------------------------- $7
IMU -------------------------------------------------------------------------------------------------------------- $8
Battery ---------------------------------------------------------------------------------------------------------- $16
Power Distribution Board ---------------------------------------------------------------------------------- $8
Bluetooth x2 --------------------------------------------------------------------------------------------------- $18
Arduino Mega 2560 ------------------------------------------------------------------------------------------ $50
Voltage Regulator --------------------------------------------------------------------------------------------- $10
Miscellaneous Screws and Wires ------------------------------------------------------------------------- $15
Controller Buttons, x8 --------------------------------------------------------------------------------------- $5
-------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Total: ~ $200

## Slide 39: What We Learned
Hardware selection is vital!
  Motors need to be powerful, reliable, and efficient:
    Power: Actually generate enough lift
    Reliability: Motors need to spin at close to the same speed
    Efficiency: The more power required, the bigger the battery must be
Understand Power Requirements
  Every system requires power; have a plan for routing power
  Be careful with voltage/current rating for individual components
  Mosfets get very hot when you run lots of power through them

## Slide 40: What We Learned (continued)
Drones are hard

## Slide 41: What We Learned (continued)
Drones are hard
fans
easy

## Slide 42: What We Learned (continued)
Drones are hard
Next time we’re making a submarine
fans
easy

## Slide 43: Demo Time!*
Please keep your hands and feet inside the classroom at all times
AWAY FROM THE DRONE
* Team 0xDEADBEEF will not be held liable for any injuries, psychological or physical, incurred during the proceedings
of this demonstration. Observe at your own risk.